## Slide 1: IDF X95 Conversion Kit

## Slide 2: Objective
Purpose
Develop a drop in conversion kit that will fully function the IWI X95 using standard FOF 5.56mm ammunition.
Customer
Israel Defense Force (IDF):
  Quantity being supplied to IDF: 1570 units
  85% RH / 15% LH configuration
  RFP #1000360168 Technical Spec. Document

## Slide 3: X95 Requirements: IDF RFP #1000360168 Technical Spec.

## Slide 4: Final Design Solution
Reduced weight steel bolt carrier with reduced recoil spring rate
Components and assembly by Creed Monarch
Creed Monarch supplies all components to IWI – Israel Prints
Painted blue in cutout features for visibility through ejection port
Bolt head diameter reduced to only fire 5.56mm FOF ammunition (no live ammunition)

## Slide 5: Results
Criteria | Pass | Fail | Specification | Actual
Accuracy (Max) | X |  | Max E.S. = 5in @ 40’ | 1.5 +/- 0.5in
Velocity (Avg) | X |  | Average: 425-525 fps | Average: 433 fps
Velocity (Std) | X |  | STD: 35 | STD: 14
Function – Semi Auto | X |  | MRBS > 350 | MRBS > 3150 # Guns Tested: 4 # Kits Tested: 5 Round Count: 6300 Confidence: > 99%
Function – Full Auto | X |  | MRBS > 350 | MRBS > 490 # Guns Tested: 3 # Kits Tested: 5 Round Count: 5400 Confidence: 77%
DVT conducted at IWI USA in Harrisburg, Pennsylvania
Testing occurred over three days in four weapons and five conversion kits
A total of four shooters consuming 14,700 rounds.

## Slide 6: Safety Design - 1
Bolt and case head interference
Reduced bolt face diameter prevents firing from other ammunition such as Sims, UTM, SRTA, and Live ammunition
Minimum Tolerance Interference Fit |  |  | 
Live | UTM | SRTA | Sims
0.021” | 0.021” | 0.006” | 0.005”
Live | Pass
SRTA | Pass
Sims | Pass
UTM | Pass

## Slide 7: Safety Design - 2
Step feature on bolt carrier prevents a live bolt to be assembled into bolt carrier
Live Bolt
Conversion Bolt
Staked bolt guide pin ensures user can not remove bolt without using Armorer tools

## Slide 8: Magazine Requirements: IDF RFP #1000360168 Technical Spec.

## Slide 9: Magazine
Molded in feature prohibits M855 or M193 to be loaded past the first round
Translucent blue tinted body with blue baseplate signifies a training magazine even when loaded in to a firearm such as an M4 or X95

## Slide 10: Pelican

## Slide 11: Pelican Foam